## Slide 1: Windows 7 and Windows Server 2008 R2 Kernel Changes
Mark Russinovich
Technical Fellow, Windows
Microsoft
CL04

## Slide 2: About Me
Technical Fellow, Microsoft
Co-founder and Chief Software Architect of Winternals Software
Co-author of Windows Internals 4th and 5th Edition and Inside Windows 2000 3rd Edition with David Solomon
Creator of Sysinternals Tools
  Now hosted on TechNet
Home of my blog and forums Contributing Editor TechNet Magazine, Windows IT Pro Magazine
Ph.D. in Computer Engineering

## Slide 3: Scope of the Talk
Talk covers key enhancements to the Windows 7 and Windows Server 2008 R2 kernel and related core components
  Performance, scalability, power efficiency, virtualization, security…
Many other significant improvements not covered:
  New taskbar (Superbar), DirectX enhancements including D2D, DWrite and DirectCompute, Home Group, Branch Cache, DirectAccess, Device Stage, PowerShell v2 and Troubleshooting Packs, User-mode Scheduling, Virtualization

## Slide 4: The Kernel
Windows 7 and Server 2008 R2 based on same kernel
As planned, Server 2008 R2 is 64-bit only
  Wow64 is an optional component on Server Core
6.1 version number for application compatibility
  Does not reflect number of major Windows NT-based releases
  Does not reflect amount of change in the system
  Anticipated that many applications would check for Vista major version (6) at the time of release

## Slide 5: Agenda
Componentization and Layering
Performance
Power Efficiency
Reliability
Security
Native VHD
Virtualization
Scalability

## Slide 6: MinWin
MinWin is first step at creating architectural partitions
  Can be built, booted and tested separately from the rest of the system
  Higher layers can evolve independently
MinWin was defined as set of components required to boot and access network
  “Cutler’s NT”: Kernel, file system driver, TCP/IP stack, device drivers, services
  No servicing, WMI, graphics, audio or shell
MinWin footprint: 150 binaries, 25MB on disk, 40MB in-memory

## Slide 7: MinWin Layering
Shell,
Graphics,
Multimedia,
Layered Services,
Applets,
Etc.
Kernel,
HAL,
TCP/IP,
File Systems,
Drivers,
Core System Services
MinWin

## Slide 8: DLL Refactoring
Required some DLLs to be “refactored” to remove dependencies on higher layers
Applications outside of MinWin use legacy DLLs
  DLLs forward calls to MinWin APIs into MinWin DLLs
  Example:
    Kernel32.dll -> Kernelbase.dll
    Advapi32.dll -> Kernelbase.dll

## Slide 9: API Sets
Problem: DLLs contain multiple API sets
  Ties API contracts with DLL implementation
API Sets are virtual DLLs
  Internal API architecture is separated from implementation
  Virtual DLLs can be combined at build time for efficiency
MinWin APIs first ones factored into virtual DLLs:
  E.g. api-ms-win-core-errorhandling-l1-1-0.dll
  Numbers are layer in the system, major and minor version of API

## Slide 10: Mapping Virtual DLLs to Logical DLLs
The mapping of virtual to logical is stored in a schema that’s embedded in Apisetschema.dll
  Kernel reads schema during boot and maps it into every process for quick lookup
  Loader refers to schema for DLL loads that are pathless to find mapping
Virtual DLLs images present on system for application compatibility with tools like Dependency Walker
  Not used by loader
Virtual DLL 1
Virtual DLL 2
ApiSetSchema.dll
Logical DLL
Loader

## Slide 11: Console Window Support
As part of re-architecture, Windows message loop for cmd.exe moved into Conhost.exe
  Was in Csrss.exe
  Also closes User Interface Privilege Isolation hole
Conhost processes keyboard input
  Is child of Csrss.exe
  Cmd.exe processes commands

## Slide 12: Agenda
Componentization and Layering
Performance
Power Efficiency
Reliability
Security
Native VHD
Virtualization
Scalability

## Slide 13: Client Footprint Reduction
Over 400 footprint reductions across all components
Chart: 
| LaptopA (x86) | LaptopB (x86) | ShipA (x86) | ShipB (x86) | ShipG (x86) | ShipH (x86) | ShipI (x86) | ShipJ (x86) | LaptopA (x64) | LaptopB (x64) | ShipB (x64) | ShipJ (x64)
Vista SP1 | 919 | 812 | 609 | 899 | 627 | 780 | 773 | 854 | 1249 | 1085 | 1198 | 1177
Windows 7 Beta | 721 | 693 | 536 | 697 | 545 | 659 | 656 | 760 | 976 | 872 | 928 | 992
MB

## Slide 14: Server Footprint Reduction
Chart: Idle Reference Set
| W2K3 | WS08 SP1 | WS08 R2
Enterprise Full | 250 | 158 | 121
Enterprise Core | 132 | 92

## Slide 15: Memory Optimizations
DWM re-architecture reduces memory footprint per window by 50%
Registry read into paged pool
  Was memory mapped before
  Improves performance because views into registry file don’t need to be mapped and unmapped

## Slide 16: Working Set Improvements
Memory manager tuned to reduce impact of run-away processes
  Processes that grow quickly reuse their own pages more aggressively
  Uses 8 aging levels (3-bits) instead of 4 (2-bits)
System cache, paged pool, and pageable system code now each have own working set
  Now, each tuned according to specific usage, which improves memory usage
  Reduces impact of file copies on system code
System Cache, Paged Pool, System Code
P1
P2
…
System Cache
P1
P2
…
Paged Pool
System Code
Vista, Server 2008
Windows 7, Server 2008 R2

## Slide 17: PerfTrack
PerfTrack: 300 user-visible scenarios identified
  Examples: open start menu, open control panel, booting
Performance goals set for each feature
  Instrumented with begin/end events
  Data sampled from Customer Experience Program and fed back to feature teams
Click Start Menu
Great
OK
Bad
Start Menu Open

## Slide 18: ReadyBoost/ReadyBoot Improvements
Kernel-mode Store Manager for tighter integration with Memory Manager
  Can now cache pagefile-backed pages
Support for 32 GB cache (4 GB in Vista)
Better security with AES256 encryption
Improved ReadyBoot to speed up boot
  Reduced memory usage such that it can run on machines < 1GB
  Compression disabled for machines > 1.7GB to save CPU

## Slide 19: PerfTrack – Start Menu
Build 7000
Build 7033

## Slide 20: Agenda
Componentization and Layering
Performance
Power Efficiency
Reliability
Security
Native VHD
Virtualization
Scalability

## Slide 21: Keys to Power Efficiency
Keep idle and stay idle
  Minimize running services and tasks
  Avoid background processing
  Let LPs and sockets stay idle so that they enter deep sleep (C states)
Chart: System Power vs. CPU Utilization (Idle)
| 0.58000000000000052 | 19.079999999999988 | 37.450000000000003 | 56.05 | 72.440000000000026 | 84.57 | 99.52
 | 15.738 | 18.2062 | 20.2162 | 22.2566 | 29.7514 | 32.0934 | 33.8587
+10% CPU = +1.25W
+1.25W = -8.3% battery

## Slide 22: Core Parking
Before, CPU workload distributed fairly evenly across LPs
  Even if utilization low
Core Parking tries to keep load on fewest LPs possible
  Allows others to sleep
  Is aware of socket topology
    Newer processors put sockets into deep sleep if cores are idle
Core Parking active on server and SMT (hyperthreaded systems only)
  Best returns on medium utilization workloads
  Clients tend to run at extremes (0 or 100)

## Slide 23: Core Parking Design
Power management timer fires periodically (30-50ms)
  Performs P-state management
  Calculates average utilization and implements core parking policy
Determines which LPs to “park” and which to “unpark”:
  Unpark cores if average for unparked is > increase threshold
  Park cores if average for unparked < decrease threshold
  Parked cores above parking threshold also unparked
  At least one CPU in each NUMA node left unparked
Power manager notifies scheduler of updated parking decision
  Scheduler avoids parked cores
    Overridden by hard affinity and thread ideal processor if no others available
  Interrupts and DPCs not affected

## Slide 24: Core Parking Operation
Socket 0
Core 0
Core 1
Core 0
Core 1
Socket 1
Core 1
Core 0
Core 0
Core 1
Workload

## Slide 25: Unified Background Process Manager (UBPM)
UBPM infrastructure unifies mechanism for event-based process start and stop
  Implemented in Service Control Manager to avoid creating another process
  All events are based on ETW events
    UBPM is a central manager of ETW consumer registration and notification
UBPM clients:
  Task scheduler: new Taskhost processes
  Service Control Manager: trigger-started services

## Slide 26: Trigger-Started Services
Before, services typically started at system boot and ran until shutdown
Services can now specify specific start and stop conditions (triggers):
  Device class arrival and removal
    Bthserv: start on bluetooth device class arrival
  IP address arrival and removal
    Lmhosts: start on first and stop on last IP address availability
  Firewall port event
    Browser: open of NS and DGM ports
  Domain join and unjoin
    W32Time: start on join, stop on unjoin
  Custom ETW event
    EFS: start on first encrypted file access
Triggers are stored in service registry key
  Use “sc qtriggerinfo” to view service triggers

## Slide 27: Timer Coalescing
Staying idle requires minimizing timer interrupts
Before, periodic timers had independent cycles even when period was the same
New timer APIs permit timer coalescing
  Application or driver specifies tolerable delay
Timer system shifts timer firing to align periods on natural frequency
Timer tick
15.6 ms
Periodic Timer Events
Windows 7
Vista

## Slide 28: Intelligent Timer Tick Distribution
Before, primary timer interrupt on LP 0 propagated timer to all other LPs
  LP0 timer updates system tick count and clock
  Timer interrupt for all LPs updates process and thread runtimes, checks for thread quantum end
  Even if LP was idle, it had to service interrupt
Now, timer system propagates timer only to processors that aren’t idle
  Also called tick skipping
  Non-timer interrupts still wake LP

## Slide 29: Other Power Improvements
Timer reduction:
  Eliminated TCP DPC timer on every system timer interrupt
  Reduced frequency of USB driver maintenance timers
Device power management:
  Support for latest Intel HD Audio low-power specifications
  Bluetooth radio enters selective suspend when connections are in sniff mode
  NIC automatically enters D3 when media is disconnected
Powercfg tool for managing performance policies
  Has /energy option for identifying power efficiency issues

## Slide 30: Analysis: Length of Idle Intervals
Windows* Vista SP1
Windows* 7 Build A
Windows* 7 Build B
Move right better
%idle time (per core Avg.)
Notes: 30

## Slide 31: Agenda
Componentization and Layering
Performance
Power Efficiency
Reliability
Security
Native VHD
Scalability

## Slide 32: Fault Tolerant Heap (FTH)
Heap corruption is a major cause of unreliability
  15% of all user-mode crashes
  30% of user-mode crashes during shutdown
  Very difficult to analyze and fix
FTH reduces impact of heap misuse
  Monitors for heap corruption crashes
  Applies mitigations dynamically
  Removes mitigation if unsuccessful
  Returns debug information for use by ISVs

## Slide 33: FTH Activation and Operation
After a process crash, FTH starts watching for additional crashes
  If process crashes four times in the next hour in Ntdll.dll, FTH applies appcompat shim
  Once shim applies, shim assigned weight and FTH monitors for successful mitigations
    If process crashes or mitigations not applied, shim weight reduced
    If process survives and mitigation applied, shim weight increased
    If shim weight goes below zero, shim removed
FTH shim operation:
  Validates all heap operations using native heap
  Keeps 4MB of freed buffers to mitigate double-frees
  Pads allocations < 4096-8 bytes by 8 bytes

## Slide 34: FTH Mitigations

## Slide 35: Process Reflection
Problem: want to capture dumps of processes that appear hung or that have leaked memory
  Don’t want to terminate process
  Don’t want to suspend process for lengthy dump operation
  Don’t want to scan device memory
Process Reflection creates clone of process for dump and analysis
  Modeled on native fork() support
  Makes copy that’s safe to memory scan
  Used by leak detection diagnostic
  Used by cross-process hang detection diagnostic

## Slide 36: Agenda
Componentization and Layering
Performance
Power Efficiency
Reliability
Security
Native VHD
Virtualization
Scalability

## Slide 37: User Account Control Levels
Windows 7 introduces 2 new UAC levels
  User can tune notification versus convenience
  Applies to protected-administrator only

## Slide 38: User Account Control Levels
High: Vista equivalent
  Prompts for: all elevations
  Prompts on: secure desktop
Medium: default
  Prompts for: non-Windows elevations
    Windows means:
      Signed by Windows certificate
      In secure location
      Doesn’t accept control command-line (e.g. cmd.exe)
  Prompts on: secure desktop
Low:
  Prompts for: non-Windows elevations
  Prompts on: standard desktop
    Avoids black flash and user can interact with desktop
    Possible appcompat issues with 3rd-party accessibility applications
Off: UAC off
  No Protected Mode IE
  No file system or registry virtualization

## Slide 39: Virtual Accounts
Want better isolation than existing service accounts
  Don’t want to manage passwords
Virtual accounts are like service accounts:
  Process runs with virtual SID as principal
    Can ACL objects to that SID
  System-managed password
  Show up as computer account when accessing network
Services can specify a virtual account
  Account name must be “NT SERVICE\<service>”
    Service control manager verifies that service name matches account name
  Service control manager creates a user profile for the account
Also used by IIS app pool and SQL Server

## Slide 40: Managed Service Accounts
Services sometimes require network identity e.g. SQL, IIS
Before, domain account was only option
  Required administrator to manage password and Service Principal Names (SPN)
  Management could cause outage while clients updated to use new password
Windows Server 2008 R2 Active Directory introduces Managed Service Accounts (MSA)
  New AD class
  Password and SPN automatically managed by AD like computer accounts
  Configured via PowerShell scripts
  Limitation: can be assigned to one system only

## Slide 41: BitLocker
Vista introduced BitLocker Drive Encryption
  Encrypts fixed volumes
  Multiple ways to store key:
    TPM, PIN, USB key, multi-factor
  Uses a volume filter driver so that encryption is transparent to system
Windows now BitLocker ready
  Always creates hidden 200 MB system partition

## Slide 42: BitLocker-to-Go
Windows 7 adds support for removable media
  Key is protected by password or smartcard
  Virtual FAT volume with drive decrypting utility makes volume accessible down level

## Slide 43: BitLocker-to-Go Format
View on Down-Level System

## Slide 44: Windows Biometric Framework (WBF)
WBF standardizes the way that biometric support software plugs into the system
  E.g. fingerprint swipe, retina scan
  Takes burden off of IHV and standardizes interfaces and UX
WBF includes:
  Core platform
  Management components
  UX components

## Slide 45: Other Security Enhancements
Object auditing improvements:
  Global access object auditing
  Reason auditing:
    Logging of ACE (Access Control Entry) that caused allow or deny
    Requires Handle Manipulation auditing
App Locker
  Kernel enforcement of policy
  More flexible image identification (e.g. certificates)

## Slide 46: Agenda
Componentization and Layering
Performance
Power Efficiency
Reliability
Security
Native VHD
Virtualization
Scalability

## Slide 47: Native VHD Support
Foundational support for booting from VHD and for Surface/Removal of VHDs
    Orderly shutdown of volumes
    Support for nested volumes (2 levels)
    Servicing for mounted (offline) VHD volumes
  VHD operations
    Create / Attach/ Detach
    Meta-operations: Merge, Expand, Compact
Tools and APIs:
  Win32 APIs
  VDS APIs (DCOM Remotable)
  Hyper-V WMI for management operations
Performance goal: within 10% of native

## Slide 48: Native VHD Architecture
Physical Volume Stack
Virtual Volume Stack
Disk
Partmgr
Volmgr
FS
Volmgr
FS
FS Depends
FS Depends
VHD Driver
User / Management Application
Win32 xxxVirtualDisk()
[Create, Surface, Remove, Merge, Compact, Convert]
*HYPER-V WMI
Diskmgmt.msc
Diskpart.exe
VDS APIs
*Requires installation of Hyper-V role

## Slide 49: Native VHD Performance
Chart: Physical Drive vs. Fixed VHD vs. Dynamic VHD vs. Passthru (VM Mode)
| 64K Sequential Read | 64K Sequential Write | 4K Random Read | 4K Random Write
Physical Drive in Host | 714.7338 | 338.3954 | 6.6688 | 10.3533
Fixed VHD in Win7 | 713.3162 | 327.9747 | 6.676 | 10.4386
Dynamic VHD in Win7 | 714.5622 | 230.4655 | 6.6747 | 8.968
Passthru in Win7 | 715.53 | 315.23 | 6.66 | 10.48

## Slide 50: VHD Boot
Strategic direction for Windows in the Data Center
  Image consolidation
    Single image format for generalized and specialized physical images
    Single generalized master image for virtual and physical environments
  Reduced management TCO
    Single toolset and process for management and deployment
Enables other compelling scenarios
  Rapid provisioning and repurposing
  Rapid, reliable patching and rollback

## Slide 51: VHD Boot in Windows
D:\
C:\
VHD
Windows

## Slide 52: Agenda
Componentization and Layering
Performance
Power Efficiency
Reliability
Security
Native VHD
Virtualization
Scalability

## Slide 53: Overview of Server 2008 R2 Hyper-V Scaling Improvements:
Many performance and scalability improvements
  Lock free algorithms
  Distributed data structures
Virtualization Feature | WS08 Hyper-V RTM | WS08 Hyper-V SP2 | Windows Server 2008 R2 Hyper-V
Logical Processor Support | 16 | 24 | 64
Total number of powered on VM’s | 128 | 192 | 384
Total Virtual Processors Supported | 128 | 192 | 512
Guest Virtual Processor Support | 4 (WS08 only) | 4 (WS08 only) | 4 (Win7/WS08)

## Slide 54: VM Migration
Planned VM migration scenarios:
  Hardware maintenance
  Load balancing for performance
  Consolidation for power
Windows Server 2008 includes Quick Migration
  VM stored on SAN managed by Microsoft Cluster Services
  Suspend of VM on one system to shared disk followed by resume on another
  Outage is time it takes to save and restore VMs memory

## Slide 55: Live Migration
Live Migration migrates a running VM with minimal disruption of the VMs services
  Goal is that open TCP/IP connections do not timeout
Live Migration steps:
  Establish connection between source and target host
  Transfer VM configuration and device information
  Transfer VM memory
  Suspend source VM and transfer state
  Resume target VM

## Slide 56: Live Migration Operation
Source
Host
Target
Host
time
Migration
Setup
Memory
Transfer
State
Transfer
VM Running

## Slide 57: Live Migration Internals
Worker process on source host creates “dirty bitmap” of memory pages
  Iterates over pages, sending them to target worker process
  Registers for modify-notifications on pages to detect subsequent changes
    Source VM still active and can be modifying memory
  Repeats over newly modified pages
Stops iterating when one of the following:
  All pages sent
  Makes 5 passes

## Slide 58: Live Migration Operation
Server 1
Server 2
Configuration
Memory
Configuration
State
State

## Slide 59: High Available Storage and Virtualization
Traditional HA storage is ‘shared nothing’ where one node exclusively owns a LUN
Shared nothing has major disadvantages for virtualization management and high availability
  One VM per LUN requirement causes LUN explosion
    Management headache
  Disruptive delays when LUN ownership changes
    Physical disk resource must fail over
    Old owner must dismount and new owner must mount volume
    Not suitable for Live Migration

## Slide 60: Clustered Shared Volumes
Clustered Shared Volumes (CSV) implements hybrid sharing for LUNs
  One node owns the storage namespace (e.g. directory structure) and metadata
  Other nodes can own the storage backing an individual file’s data (e.g. VHD)
Benefits of CSV:
  Can store all VM VHDs on one LUN
  High-performance access to VHDs from owning nodes
    All nodes have read/write access to file data
  Seamless VM movement between nodes
    Any node can read from VHD, so no need to change LUN ownership
  Seamless LUN ownership transition
    Persistent handles allow cluster to move LUN without interruption to VM operation

## Slide 61: Clustered Shared Volume Implementation
CSV filter driver forwards all namespace operations (e.g. create file, delete file, resize file) to LUN owner
  These operations are relatively rare
  Uses SMB2
VM hosting node opens VHD for exclusive access
  VHD read and write is frequent
  CSV filter obtains raw LUN sector map of file
  Reads and writes directly to underlying volume

## Slide 62: Clustered Shared Volumes Architecture
LUN
CSV I/O Filter Driver
Redirector FSD
NetFT
Storage Drivers
CSV I/O Filter Driver
NTFS
NetFT
Storage Drivers
File Server Service
CreateFile
VM
VHD
LUN Owner

## Slide 63: Clustered Shared Volumes Architecture
LUN Owner
LUN
CSV I/O Filter Driver
Redirector FSD
NetFT
Storage Drivers
CSV I/O Filter Driver
NTFS
NetFT
Storage Drivers
File Server Service
Read/WriteFile
VM
VHD

## Slide 64: CSV Scalability
1000 VMs running on a 16-node cluster with 16.5 TB shared storage:

## Slide 65: VM Memory Management
Today, processors provide one level of address translation, but hypervisor needs to manage two
Guest Virtual Address
Guest Physical Address
System Physical Address
Guest OS defines GVA-to-GPA mappings
Hypervisor defines GPA-to-SPA mappings
Guest Virtual Address
System Physical Address
Shadow page tables combine these mappings because the processor knows how to perform only one level of translation

## Slide 66: Shadow Page Tables
Hypervisor maintains a Shadow Page Table
  Combines two layers of translation into a single page table
  Demand-filled when Child OS touches a page
  Flushed any time the Child OS modifies its page tables
Shadow Page Table overhead:
  Fills and flushes invoke the hypervisor
  Can account for up to 10% of total CPU time
  Typically consumes 10-30 MB of memory per VM

## Slide 67: Second Level Address Translation (SLAT)
Goes by several names:
  Intel calls it Extended Page Tables (EPT)
  AMD calls it Nested Page Tables (NPT) or Rapid Virtualization Indexing (RVI)
Processor provides two levels of translation
  Walks the guest OS page tables directly
  No need to maintain Shadow Page Table
  No hypervisor code for demand-fill or flush operations
Resource savings:
  Hypervisor CPU time drops to 2%
  10-30 MB of memory saved per VM

## Slide 68: Agenda
Componentization and Layering
Performance
Power Efficiency
Reliability
Security
Native VHD
Virtualization
Scalability

## Slide 69: Distributed Timer Execution
Before, all timer expiration (deferred procedure calls – DPCs) executed on CPU 0
Relying on one CPU for DPC timer expiration can cause bottleneck on Hyper-V servers with many guests:
  Root timers execute on CPU 0 and the more guests, the more timers
  CPU 0 can also execute guest virtual processors, reducing time it can execute timers
  Worse, overload of CPU 0 could result in DPC timeouts and delayed timers
CPU 0
CPU 1
CPU 2
CPU 3
Global
Timer
Queue

## Slide 70: Distributed Timer Execution (Cont)
Now, timers execute on the processor on which they are inserted
Major scalability benefit
  Spreads timer DPC load across CPUs
  No global timer lock
  Note: timers on parked cores migrate on next expiration and old behavior on client
CPU 0
CPU 1
CPU 2
CPU 3
Per-CPU
Timer
Queues

## Slide 71: Simultaneous Multithreading
Simultaneous Multithreading (SMT or Hyperthreading):
  Physical core presents multiple logical processors
  Duplicates certain CPU execution engines
Scheduler has been SMT-aware since Windows XP
  Avoids doubling up logical pairs when a physical core is idle
Scheduler has SMT improvements in Windows 7:
  Idle core preferred to ideal logical processor for placement of thread at scheduling time
  Migrates threads at quantum-end to idle cores
  Uses “SMT Parking” as a further guide for avoiding use of logical pairs
23% performance gain for Windows Media Encoder 9.0 (Windows 7 vs. Windows Vista SP1)

## Slide 72: SMT Parking Operation
Core 0
Core 2
Workload
Core 1
LP 0
LP 1
Core 3
LP 0
LP 1
LP 0
LP 1
LP 0
LP 1
LP 1
LP 1
LP 1
LP 1

## Slide 73: Dynamic Fair Share Scheduling (DFSS)
Before, no quality of service for Remote Desktop (formerly called Terminal Server) users
  One user could hog server’s CPU
Now, Remote Desktop role automatically enables DFSS
  Sessions are given weight 1-9 (default is 5)
    Internal API can set weight
Each session given CPU budget
  Over 150ms interval: Cycles per Interval / Total Weights * Session Weight
  Budget charge happens at every scheduler event
When session exceeds quota, its threads go to idle-only queue
  Scheduled only when no other session wants to run
  At end of interval, all threads made ready to run

## Slide 74: Other Scheduling Policy Improvements
Load Balancing enhancements
  Scheduler implements local maxima scheduling for performance
  Leads to inversions - high priority threads can wait while low priority threads run
  Balance set manager now periodically examines busy NUMA nodes and migrates threads to ensure higher priority threads execute
Work stealing algorithm enhanced
  Avoids scanning idle processors, increasing idle residency
  Threads stolen from closer NUMA nodes first, limiting the migration penalty
Foreground boost handoff improvements
  Ensure foreground priority boost maintained in common priority inheritance scenarios
  Improves responsiveness for client MP systems
Boosting removed from unfair locks
  Prevents priority boost proliferation
  Eliminates unnecessary preemptions

## Slide 75: User Mode Scheduling (UMS)
Avoiding lock contention gives the best scaling
Cooperative scheduling in user-mode avoids contention and context switches
Limitation of Fibers is that the kernel doesn’t know about them
  Some system calls have state associated with underlying thread
  If Fibers make system calls, state can become corrupt

## Slide 76: UMS (Cont)
UMS solves thread state problem by separating user-mode thread and kernel-mode thread
  Switching between user-threads doesn’t switch kernel thread
  When a user-mode thread goes into kernel mode, it switches to the corresponding kernel thread
Concurrent runtimes like ConcRT (Visual Studio) use UMS

## Slide 77: Thread Scheduling vs UMS
Core 2
Thread
3
Non-running threads
Core 1
Thread
4
Thread
5
Thread
1
Thread
2
Thread
6
Core 2
Core 1
User
Thread
2
Kernel
Thread
2
User
Thread
1
Kernel
Thread
1
User
Thread
3
Kernel
Thread
3
User
Thread
4
Kernel
Thread
4
User
Thread
5
Kernel
Thread
5
User
Thread
6
Kernel
Thread
6
Thread Scheduling
Cooperative Scheduling

## Slide 78: Windows and Logical Processors
Before, the maximum number of Logical Processors (LPs) was dictated by word size
  LP state (e.g. idle, affinity) represented in word-sized bitmask
  32-bit Windows: 32 LPs
  64-bit Windows: 64 LPs
0
16
31
32-bit Idle Processor Mask
Idle
Busy

## Slide 79: Windows and Logical Processors (Cont)
With many-core, systems with > 64LPs will become more common
  8 socket, six core, 2x SMT (hyperthreaded): 96 LPs
Need to support > 64LP while preserving compatibility

## Slide 80: > 64 LP Support
Solution: LPs divided into Groups
  Group can have a maximum of 64 LPs
  Maximum of 4 Groups (for maximum of 256 LPs)
Group assignment:
  One group if 32-bit system or fewer than 65 LPs
  Otherwise fewest groups necessary to ensure that NUMA nodes don’t cross groups
    Close NUMA nodes kept in the same group

## Slide 81: Processor Groups
Example: 4 LPs/core, 4 cores/socket, 2 sockets/node, 4 nodes: 128 LPs
Group
NUMA Node
Socket
Core
LP
LP
LP
LP
Core
LP
LP
LP
LP
Core
LP
LP
LP
LP
Core
LP
LP
LP
LP
Socket
Core
LP
LP
LP
LP
Core
LP
LP
LP
LP
Core
LP
LP
LP
LP
Core
LP
LP
LP
LP
NUMA Node
Socket
Core
LP
LP
LP
LP
Core
LP
LP
LP
LP
Core
LP
LP
LP
LP
Core
LP
LP
LP
LP
Socket
Core
LP
LP
LP
LP
Core
LP
LP
LP
LP
Core
LP
LP
LP
LP
Core
LP
LP
LP
LP
Group
NUMA Node
Socket
Core
LP
LP
LP
LP
Core
LP
LP
LP
LP
Core
LP
LP
LP
LP
Core
LP
LP
LP
LP
Socket
Core
LP
LP
LP
LP
Core
LP
LP
LP
LP
Core
LP
LP
LP
LP
Core
LP
LP
LP
LP
NUMA Node
Socket
Core
LP
LP
LP
LP
Core
LP
LP
LP
LP
Core
LP
LP
LP
LP
Core
LP
LP
LP
LP
Socket
Core
LP
LP
LP
LP
Core
LP
LP
LP
LP
Core
LP
LP
LP
LP
Core
LP
LP
LP
LP

## Slide 82: 256 Processor System

## Slide 83: Processes, Threads, and Groups
By default, processes are affinitized to have all threads run in a single group
  Thread can be affinitized to only the CPUs within a single group
Group Assignment:
  Processes assigned group and ideal node round-robin
  By default, thread assigned ideal CPU from process’ ideal node round-robin
  Legacy affinity APIs apply at group level
Application can take advantage of > 64 LPs by assigning threads to a different group than default

## Slide 84: NUMA Enhancements
Support for NUMA has improved every release
  Scheduler more NUMA aware
  Memory Manager more NUMA aware
New APIs for:
  Getting relationships between caches, cores, sockets, nodes, and groups (topology)
  Mapping LPs to NUMA nodes and vice versa
  Getting distance between NUMA nodes
Services can specify ideal NUMA node

## Slide 85: Removal of the Memory Manager PFN Lock
Windows tracks the state of pages in physical memory
  In use (in a working set)
  Not assigned to a working set (on one of several paging lists: free, zero, modified, standby…)
Before, all page state changes protected by global PFN (Physical Frame Number) lock
Now, the PFN lock is gone
  Pages are now locked individually
  Improves scalability for applications that manage large amounts of memory

## Slide 86: Removal of Other Major Locks
Cache Manager Virtual Address Control Block (VACB) lock
  Not completely removed, but gone from common code paths
  Improves scaling of applications that perform intensive cached file I/O
Object Manager Type lock
  Improves scaling of workloads that modify kernel objects (synchronization, files, registry keys)

## Slide 87: Removal of the Dispatcher Lock
Locks serialize access to data structures
  Prevents multiple threads from simultaneously modifying data
  Inhibits scaling because threads must wait for their turn (contention)
Scheduler Dispatcher lock hottest on server workloads
  Lock protects all thread state changes (wait, unwait)
To improve scaling, lock was removed
  Each object protected by its own lock
  Many operations are lock-free

## Slide 88: Scaling Without the Dispatcher Lock
1.7x scaling going from 128 to 256 LPs:
Chart: 
| 128 LP | 256 LP
Fibers | 1193 | 2023
Threads | 1208 | 2001
OLTP Workload Throughput
Transactions/minute

## Slide 89: Summary and More Information
Lots of exciting kernel changes in Windows 7 and Server 2008 R2!
  There’s more that I didn’t have time to cover
  Faster, more scalable, more secure
Further reading:
  MSDN (SDK and WDK) describes new user and kernel mode APIs
  Look for my upcoming kernel changes blog post series
  Windows Internals 6th Edition (2010)

## Slide 90
YOUR FEEDBACK IS IMPORTANT TO US!
Please fill out session evaluation forms online at
MicrosoftPDC.com

## Slide 91: Learn More On Channel 9
Expand your PDC experience through Channel 9
Explore videos, hands-on labs, sample code and demos through the new Channel 9 training courses
  channel9.msdn.com/learn
Built by Developers for Developers….